## Slide 1: Actuator based on synchronous motor drive
Sergey Lovlin , Dmitriy Lukichev, Nikolay Polyakov
Faculty of Control Systems and Industrial Robotics , ITMO University , Saint Petersburg

## Slide 2: Content
Mathematical description of a synchronous motor without damper winding
Mathematical description of a synchronous motor with permanent magnets
Vector control for PMSM
Brushless DC motor

## Slide 3: Mathematical description of a synchronous motor without damper winding
Faculty of Control Systems and Industrial Robotics , ITMO University , Saint Petersburg

## Slide 4
Model of a synchronous motor in a rotating coordinate system
  Rs – resistance of stator windings
  Lsd , Lsq – stator winding inductances along the d- and q- axes. Special case of non-salient pole design of the motor rotor Ld = Lq = Ls
  Isd , Isq, Usd , Usq – stator winding currents and voltages along the d- and q- axes
  Rf – resistance of excitation winding
  Lf – inductance of excitation winding
  Mdf – mutual induction coefficient between the field winding and the stator winding along the d axis

## Slide 5
Model of a synchronous motor in a rotating coordinate system
  Dynamic model:
  Ψf – flux of excitation winding
  Ω – mechanical speed
  ω – electrical speed
  Zp – pole pairs
  Ψsd – flux of stator winding along axis d
  Ψsq – flux of stator winding along axis q
  ω0 – angular frequency of stator voltages

## Slide 6
Model of a synchronous motor in a rotating coordinate system
  Dynamic model:
  Ψf – flux of excitation winding
  Ψsd – flux of stator winding along axis d
  Ψsq – flux of stator winding along axis q
  Ω – mechanical speed
  ω – electrical speed
  Zp – pole pairs
  ω0 – angular frequency of stator voltages
  Tme – magnetoelectric torque of synchronous motor

## Slide 7
Model of a synchronous motor in a rotating coordinate system
  Magnetoelectric torque:
  Second Newton’s law:
  Ω – mechanical speed
  Tme – magnetoelectric torque of synchronous motor
  Tdist – disturbance torque
  ω – electrical speed (angular speed of rotor flux Ψf )
  Let’s consider:
  Then:
  θ – angle of the load (angle between stator flux Ψs and rotor flux Ψf )

## Slide 8
Model of a synchronous motor in a rotating coordinate system

## Slide 9
Model of a synchronous motor in a rotating coordinate system

## Slide 10
Model of a synchronous motor in a rotating coordinate system
  general torque Tme1
  Reactive torque of a salient-pole motor Tme2

## Slide 11
Model of a synchronous motor in a rotating coordinate system
  1 - generator mode
  2 - motor mode

## Slide 12
Model of a synchronous motor in a rotating coordinate system
  Let:
  Then:

## Slide 13: Mathematical description of a synchronous motor with permanent magnets
Faculty of Control Systems and Industrial Robotics , ITMO University , Saint Petersburg

## Slide 14
Mathematical description of a synchronous motor with permanent magnets
  Assumptions:
  - no magnetic circuit saturation, iron losses, current displacement effect
  - stator windings are symmetrical
  - leakage inductance does not depend on the position of the rotor in space

## Slide 15
Mathematical description of a synchronous motor with permanent magnets
  Rs – resistance of stator windings
  Ld , Lq – stator winding inductances along the d- and q- axes. Special case of non-salient pole design of the motor rotor Ld = Lq = Ls
  Id , Iq, Ud , Uq – stator winding currents and voltages along the d- and q- axes

## Slide 16
Model of a synchronous motor in a rotating coordinate system
  Dynamic model:
  Ψf – flux of permanent magnets
  Ω – mechanical speed
  ω – electrical speed
  Zp – pole pairs
  Ψd – flux of stator winding along axis d
  Ψq – flux of stator winding along axis q
  J – inertia
  β – viscous friction coefficient

## Slide 17
Model of a synchronous motor in a rotating coordinate system
  Dynamic model:
  Ψf – flux of permanent magnets
  Ω – mechanical speed
  ω – electrical speed
  Zp – pole pairs
  Ψd – flux of stator winding along axis d
  Ψq – flux of stator winding along axis q
  J – inertia
  β – viscous friction coefficient
  Tme , Tdist – magnetoelectric and disturbance torque

## Slide 18: Vector control for PMSM
Faculty of Control Systems and Industrial Robotics , ITMO University , Saint Petersburg

## Slide 19
Vector control for PMSM
  Field of application:
  high-quality electric drive for metal-cutting machines.
  Features:
  speed control range (D): more than 10000
  speed control bandwidth (fc): more than 100 Hz

## Slide 20
Vector control for PMSM
  Dynamic model:
  Rs – resistance of stator windings
  Ld , Lq – stator winding inductances along the d- and q- axes. Special case of non-salient pole design of the motor rotor Ld = Lq = Ls
  Id , Iq, Ud , Uq – stator winding currents and voltages along the d- and q- axes
  J – inertia
  β – viscous friction coefficient
  Ψf – flux of permanent magnets
  Ω – mechanical speed
  ω – electrical speed
  Zp – pole pairs
  Tdist – magnetoelectric and disturbance torque

## Slide 21
Vector control for PMSM

## Slide 22
Vector control for PMSM
  Coordinate transformation:

## Slide 23
Vector control for PMSM
  Coordinate transformation:
  Let’s assume:
  Then:

## Slide 24
Vector control for PMSM
  Switch control:
  TS – switching commutation period
  ta.h, ta.l – opening time of the upper and lower power switches in phase A
  γa.h, γa.l – the relative opening duration of the upper and lower power switches in phase A

## Slide 25
Vector control for PMSM
  Cross-connection compensation:
  Dynamic model:

## Slide 26
Vector control for PMSM
  Current loop for d-axis:
  Current loop for q-axis:

## Slide 27: Linear optimum
  - the desired open-loop transfer function that corresponds to tuning to a linear optimum.
  - the desired transfer function of the closed system, which corresponds to the setting for a linear optimum.
Astaticism order: | 1
Transient time (95%): | ttr = 3Tt
Oscillation index: | M = 1
Overshoot: | δymax = 0

## Slide 28: Principle of calculation of regulator parameters
  - desired transfer function of the controller.
  - transfer function of the object model.
  - transfer function of feedback (sensors and measurement channel).

## Slide 29: Principle of calculation of regulator parameters
  - the desired open-loop transfer function that fits to the desired optimum.

## Slide 30
Vector control for PMSM
  Calculation of regulator parameters of current loop of d-axis:
  - the desired open-loop transfer function that corresponds to tuning to a linear optimum.
  - transfer function of the electrical part of motor

## Slide 31
Vector control for PMSM
  Calculation of regulator parameters of current loop of d-axis:

## Slide 32
Vector control for PMSM
  Analogically, calculation of regulator parameters of current loop of q-axis:

## Slide 33
Vector control for PMSM
  Calculation of regulator parameters of speed loop :

## Slide 34: Symmetric optimum
Astaticism order: | 2
Transient time (95%): | ttr = 14.7Tμ
Oscillation index: | M = 1.68
Overshoot: | δymax = 0. 43
  - the desired open-loop transfer function that corresponds to tuning to a symmetric optimum.
  - the desired transfer function of the closed system, which corresponds to the setting for a symmetric optimum.

## Slide 35
Vector control for PMSM
  Calculation of regulator parameters of speed loop :
  - the desired open-loop transfer function that corresponds to tuning to a symmetric optimum.
  - transfer function of the electrical part of motor

## Slide 36
Vector control for PMSM
  Calculation of regulator parameters of speed loop :

## Slide 37: Brushless DC motor
Faculty of Control Systems and Industrial Robotics , ITMO University , Saint Petersburg

## Slide 38
Brushless DC motor

## Slide 39
Brushless DC motor

## Slide 40
Equations for a three-phase system of motor currents:
Brushless DC motor
Back-EMF:
Torque:
  Rs – resistance of stator windings
  Ls (φr) – stator winding inductance.
  ia , ib, ic– stator winding currents
  ua, ub, uc– stator winding voltages
  ea, eb, ec– phase back EMFs
  ce– back EMF constant

## Slide 41
Equations for non-salient pole design of the motor rotor:
Brushless DC motor
Back-EMF:
Torque:
  Rs – resistance of stator windings
  Ls (φr) – stator winding inductance.
  ia , ib, ic– stator winding currents
  ua, ub, uc– stator winding voltages
  ea, eb, ec– phase back EMFs
  ce– back EMF constant

## Slide 42
Brushless DC motor
Three phase system of back-EMF:
Torque:
Let:

## Slide 43
Brushless DC motor
Three phase system of back-EMF:
Torque:
Let:

## Slide 44
Rack of three-phase inverter:
Brushless DC motor
  TS – switching commutation period
  th, tl – opening time of the upper and lower power switches in three-phase inverter rack
  γh, γl – the relative opening duration of the upper and lower power switches in three-phase inverter rack

## Slide 45
Rack of three-phase inverter:
Brushless DC motor
  TS – switching commutation period
  th, tl – opening time of the upper and lower power switches in three-phase inverter rack
  γh, γl – the relative opening duration of the upper and lower power switches in three-phase inverter rack

## Slide 46
Sine pulse-width modulation (SPWM)
Brushless DC motor
Rack of three-phase inverter:

## Slide 47
Equations for non-salient pole design of the motor rotor with SPWM:
Brushless DC motor

## Slide 48
Space vector modulation (SVM)
Brushless DC motor
Rack of three-phase inverter:

## Slide 49
Equations for non-salient pole design of the motor rotor with SPWM:
Brushless DC motor

## Slide 50
Brushless DC motor
Let’s consider equations for non-salient pole design of the motor rotor with SPWM:
Analogically:

## Slide 51
Brushless DC motor
Let’s sum this equations:
Neglecting the last term:

## Slide 52
Brushless DC motor
Speed/torque characteristic without neglecting last term:
Speed/torque characteristic with neglecting the last term:

## Slide 53
Brushless DC motor:
Vector control:
Im = var
ψ = var
Id = var
Iq = var
Brushless DC motor
Comparing with vector control

## Slide 54
  Cross connection compensation:
  Dynamic model:
Vector control:
Brushless DC motor:
Brushless DC motor